Overview
A) Power on or reset
B) 1st stage boot loader
C) 2nd stage boot loader
D) Operate system

---
Power on or reset
-The chipset sends a reset signal to the CPU until it recives a power good signal from power suply
-The CPU loads the bios boot program at address FFFF0h (CS:IP F000:FFF0) at the end of the 1MB system memory (real mode access)
-The CPU jumps to the real BIOS startup program

---
1st stage boot loaders
The 1st stage boot loader perform initial devices setup to load the 2nd stage boot loader and there are few ones:
  - BIOS
  - UEFI
  - OpenBIOS
  - OpenBoot
  - SLOF

---
Basic Input Output System (BIOS)
- Checks the CMOS (Its own ROM)
- Loads interrupt handlers
- Checks if its a cold boot or reboot (1234h at memory address 0000:0472)
- Performs the POST (PowerOn Self Test) if is a cold boot
- Loads the video card's BIOS
- Checks for other device's BIOS
- Displays startup screen
- More checks and error display
- Performs a hardware inventory
- Initializes PnP devices if supported
- Finds boot device, loads the MBR into memory and jumps to the boot code

---
BIOS: see also
- 1-http://en.wikipedia.org/wiki/BIOS_interrupt_call Full list of BIOS interrupts and services
- 2-http://en.wikipedia.org/wiki/Input/output_base_address BIOS addresses
- 3-http://www.bioscentral.com/misc/biosservices.htm# Full list of BIOS interrupts and type (Hard or soft)
- 4-http://en.wikipedia.org/wiki/INT_13H The interrupt used to load the MBR but it does low level disk services

---
 [Unified] Extensible Firmware Interface ([U]EFI)
- Software interface between OS and firmware
- Advantages
  - Ability to boot from large disks (over 2 TiB)
  - Faster boot-up
  - CPU-independent architecture
  - CPU-independent drivers
  - Flexible pre-OS environment
  - Modular design
- Replace MBR by GUID Partition Table (GPT)
- EFI provides a shell environment. The shell can be used to execute other EFI applications

---
Other 1st stage boot loaders
- OpenBIOS: http://en.wikipedia.org/wiki/OpenBIOS
- OpenBoot: http://en.wikipedia.org/wiki/OpenBoot
- SLOF: http://en.wikipedia.org/wiki/OpenBIOS#SLOF

---
2nd stage boot loaders
The second stage boot loaders can read from hard drive partitions, performs the requirements to load and give control to the OS and there are many:
- LILO
- GRUB
- Windows loader
- ….

---
GRUB and MBR
GRUB must fit into 446 bytes because

---
GRUB2: core.img
- The code in MBR loads the core.img file placed just after MBR
- Configures PXE, nfs, LVM or others if needed
- Loads and execute the module /boot/grub/normal.mod

---
GRUB2: normal.mod
- Registers command menuentry
- Loads parser.grub usualy is /boot/grub/sh.mod
- Reads /boot/grub/grub.cfg and pass it to the parser
- Shows the menu to the user if required
- Passes the contents of the {…} block for the booting menu-entry
- Invokes the “boot” command from the boot.mod module, which loads the kernel image to memory an executes it

---
Linux: startup routine
Startup routine setup minimal hw, decompress the kernel, loads initrd image and boots the kernel

---
Linux: continuation
- Initilizes devices
- Mounts initrd if any
- Boots the rest of the kernel
- Starts idle process for each CPU
- Pre-emptive scheduler is started
- Mounts real root if initrd is used

---
Linux: init function
- This function creates an init thread
- Is the 1st user space process (PID=1)
- Every process started by a user is child of init
- Executes /sbin/init or the user specified program
  - /sbin/init performs:
    - reads /etc/inittab
    - Runs boot scripts
    - switches to default runlevel

---
Linux: see also
http://www.xml.com/ldd/chapter/book/ch16.html#t3 Nice details on how kernel boot works

---
Resume

---
References
- 1-http://www.pcguide.com/ref/mbsys/bios/bootSequence-c.html
- 2-http://en.wikipedia.org/wiki/Booting
- 3-http://computer.howstuffworks.com/bios2.htm
- 4-http://en.wikipedia.org/wiki/Unified_Extensible_Firmware_Interface
- 5-http://people.apache.org/~skitching/MineOfInformation/linux/Booting_Linux_on_x86_with_Grub2.html
- 6-http://www.ibm.com/developerworks/linux/library/l-linuxboot/